Slide 1:

Welcome!

Accessibility and the ADA: Facilities Standards Update will begin at 2:00 p.m. Eastern Time

Slide 2

Listening to the Webinar

- Online:

  - Please make sure your computer speakers are turned on or your headphones are plugged in

  - Control the audio broadcast via the AUDIO & VIDEO panel

  - If you have sound quality problems, please go through the Audio Wizard by selecting the microphone icon

[Image: arrow points to microphone icon on audio and video panel]

Slide 3

Listening to the Webinar (cont.)

To connect by telephone:

1-443-453-0034

Pass Code:

368564

This is not a toll-free number

Slide 4

Captioning

- Real-time captioning is provided; open the window by selecting the “cc” icon in the Audio & Video panel

  - You can re-size the captioning window, change the font size, and save the transcript

[Image: arrow points to the "cc" icon in the audio and video panel]

Slide 5

Submitting Questions

- In the webinar:

  - Double-click on “Mid-Atlantic ADA Center” in the Participant List to open a tab in the Chat panel (keyboard: F-6 and arrow up or down to find Mid-Atlantic ADA Center); type your question in the text box and “enter”

    - Your question will be sent to the presenters; other participants will not be able to see it

- E-mail: training@transcen.org

[Image: participant list and chat box]

Slide 6

Technical Assistance

- If you experience technical difficulties

  - Use the Chat panel to send a message to the Mid-Atlantic ADA Center

  - E-mail training@transcen.org

  - Call 301-217-0124

Slide 7

Archive

- This webinar is being recorded and can be accessed within a few business days

  - ADA Hospitality Initiative website:

    - http://adainfo.org/content/AccessibilityandADAWebinars

Slide 8:

Accessibility and ADA: Facility Standards Update

Technical Specifications: Chapters 3 - 7

Slide 9:

Today’s Agenda

Chapter 3: Building Blocks

Chapter 4: Accessible Routes

Chapter 5: General Site and Building Elements

Chapter 6: Plumbing Elements and Facilities

Chapter 7: Communication Elements

Questions

Slide 10:

Chapter 3: Building Blocks

Highlights

Slide 11:

What’s in Chapter 3?

- 301 General

- 302 Floor or Ground Surfaces

- 303 Changes in Level

- 304 Turning Space

- 305 Clear Floor or Ground Space

- 306 Knee and Toe Clearance

- 307 Protruding Objects

- 308 Reach Ranges

- 309 Operable Parts

Slide 12:

Changes in Level

- 1991: [Figure illustrates a 1/4 inch vertical change in level; figure illustrates a change in level between 1/4 inch and 1/2 inch, beveled at a ratio of 1:2]

- 2010: [Figure 303.3 illustrates a vertical change in level of 1/4 inch combined with an additional 1/4 inch change in level, beveled at a ratio of 1:2, for a total change in level of 1/2 inch]

Slide 13:

Knee Clearance

- 1991: Knee/toe clearances specified in various sections

- 2010: All knee/toe clearance requirements refer to “Building Blocks” section 306

[Figure shows knee clearance 11 inches deep minimum at 9 inches above the finish floor, and 8 inches deep minimum at 27 inches above the finish floor; toe clearance is 9 inches above the finish floor.]

Slide 14:

Reach Range

- 1991:

  - Forward approach: high 48” AFF max.; 15” AFF min.

  - Side approach: high 54” AFF max.; low 9” AFF min.

- 2010: Same for forward or side approach

  - High 48” AFF max.; low 15” AFF min.

- Advisory for children’s reach ranges, based on age groups

Slide 15:

Reach

[Figure 308.2.1 illustrates an unobstructed forward reach: high of 48 inches maximum and 15 inches minimum above the floor]

[Figure 308.3.1 illustrates an unobstructed side reach: high of 48 inches maximum and 15 inches minimum above the floor]

Slide 16:

Chapter 4: Accessible Routes

Highlights

Slide 17:

What’s in Chapter 4?

- 401 General

- 402 Accessible Routes

- 403 Walking Surfaces

- 404 Doors, Doorways, and Gates

- 405 Ramps

- 406 Curb Ramps

- 407 Elevators

- 408 Limited Use / Limited Application Elevators (LULAs)

- 409 Private Residence Elevators

- 410 Platform Lifts

Slide 18:

Routes on Sites [Image indicates scoping provisions]

- New exceptions for accessible routes from site arrival points and within sites where the only means of access is by vehicle

Slide 19:

Routes between Stories [Image indicates scoping provisions]

- New exceptions related to certain multi-story buildings

  - Two-story public building, one story with occupant load of 5 or fewer people and no public use space

  - Detention/correctional facilities, residential facilities, and multi-story accessible transient lodging guest rooms: route not required to stories not containing or serving spaces required to be accessible

  - Air traffic control tower cabs and floor below

- Exceptions are for the routes to the stories only, not for the spaces or elements on the stories

Slide 20:

Routes between Spaces and Elements [Image indicates scoping provisions]

- New and revised exceptions

  - “Adaptability” allowed for raised courtroom employee stations (judge’s benches, court reporter’s stations, etc.)

    - NOT for raised public areas (jury boxes, witness stands, attorney areas, etc.)

  - Accessible route to press boxes, except …

    - Located in bleachers, points of entry at one level, aggregate area of all press boxes in facility 500 square feet maximum

    - Free-standing, elevated above grade 12 feet minimum, aggregate area of all press boxes in facility 500 square feet maximum

Slide 21:

Routes in Employee Work Areas [Image indicates scoping provisions]

- Common use circulation paths in employee work areas must be accessible except …

  - Located within areas that are less than 1000 square feet and defined by permanently installed partitions, counters, casework, or furnishings

  - Located within areas that are an integral component of work area equipment

  - Located within exterior areas that are fully exposed to the weather

[Image: bottling factory]

Slide 22:

Accessible Entrances [Image indicates scoping provisions]

- 1991: 50% of public entrances, and …

  - Relationship to number of exits required by local codes

  - At least one on ground floor

- If direct connection from parking garage, at least one accessible

- 2010: 60% of public entrances

  - No relationship to exits required by local codes

  - No requirement for ground floor entrance

- If direct connection from parking structure, all accessible

Slide 23:

Doors

- Revised specifications for maneuvering clearances

- Clarification of “recessed” doors

[Figure shows where a recess greater than 8 inches is located outside the maneuvering clearances required for forward approach to a door.]

Slide 24:

Elevators

- New provisions for standard elevators, destination-oriented elevators, and existing elevators

- New sections for limited-use/limited application (LULA) elevators, and residential elevators

Slide 25:

LULAs [Image indicates scoping provisions]

- Limited Use/Limited Application (LULA) elevators can be used …

  - Wherever full passenger elevators are not required

  - Wherever platform lifts are allowed

  - Within multi-story residential dwelling units

Slide 26:

Chapter 5: General Site and Building Elements

Highlights

Slide 27:

What’s in Chapter 5?

- 501 General

- 502 Parking Spaces

- 503 Passenger Loading Zones

- 504 Stairways

- 505 Handrails

Slide 28:

Accessible Parking [Image indicates scoping provisions]

- New Exemption:

  - Spaces used exclusively for buses, trucks, other delivery vehicles, law enforcement vehicles, or vehicular impound are not required to include accessible spaces as long as public-access lots have accessible passenger loading zones

[Image: delivery truck]

Slide 29:

Valet Parking [Image indicates scoping provisions]

- 1991:

  - Exception for valet parking facilities; accessible spaces not required

- 2010:

  - NO exception for valet parking facilities; accessible spaces required

Slide 30:

Van-Accessible Parking [Image indicates scoping provisions]

- 1991:

  - Van-accessible: one of every eight accessible spaces

- 2010:

  - Van-accessible: one of every six, or fraction of six, accessible spaces

Slide 31:

Van-Accessible Parking Configuration

- 1991: Van-accessible space has wider aisle [Image: diagram shows two accessible parking spaces with a 96 inch wide access aisle between them, for van-accessibility]

- 2010: Wider space instead of wider aisle for van spaces [Image: Fig. 502.2 shows a van parked in a space 132 inches wide and a car parked in a space 96 inches wide. The two parking spaces share an access aisle between them; it’s width is unmarked in this illustration, but it is 60 inches wide.]

Slide 32:

Access Aisles

- Must be marked to discourage parking in them

- Angled van-accessible parking space access aisles must be on passenger side

Slide 33:

Parking: Signs [Image indicates scoping provisions]

- New exemptions

  - Signs not required on sites with four or fewer total parking spaces (including accessible spaces)

  - Signs not required for residential facilities where parking spaces are assigned to specific dwelling units

[Image: parking signs with International Symbol of Accessibility]

Slide 34: [Image indicates scoping provisions]

Passenger Loading Zones

- At least one accessible passenger loading zone still required at medical care facilities, but no longer required to be “protected from the weather by canopy or roof overhang”

- New requirement for accessible passenger loading zone at vehicle drop-off and pick-up areas at mechanical access parking garages

Slide 35:

Chapter 6: Plumbing Elements and Facilities

Highlights

Slide 36:

What’s in Chapter 6?

- 601 General

- 602 Drinking Fountains

- 603 Toilet and Bathing Rooms

- 604 Water Closets and Toilet Compartments

- 605 Urinals

- 606 Lavatories and Sinks

- 607 Shower Compartments

- 608 Grab Bars

- 609 Seats

- 610 Washing Machines and Clothes Dryers

- 611 Saunas and Steam Rooms

Slide 37:

Drinking Fountains

- 1991:

  - Parallel approach allowed for certain wheelchair-accessible units

- 2010:

  - Forward approach, centered on unit, and knee and toe clearances required for all wheelchair-accessible units

    - Exception for children’s units

  - New specification for spout height for “high” fountains (for standing people):

    - 38” – 43” above floor

[Image: water fountain spout]

Slide 38:

Toilets, Toilet Rooms, and Toilet Compartments [Image indicates scoping provisions]

- New Exceptions

  - 50% (rather than all) of “clustered” single-user toilet rooms must be accessible

    - Still 5% for clustered portable single-user toilet or bathing units

  - Toilet rooms in critical or intensive care patient sleeping rooms in medical facilities are NOT required to be accessible

Slide 39:

Ambulatory-Accessible Compartments [Image indicates scoping provisions]

- Still required where there are six or more toilet compartments provided, or where there are total of six or more toilets and urinals combined

[Image: Figure shows ambulatory-accessible toilet compartment with width between 35 inches and 37 inches, depth of 60 inches minimum, and parallel grab bars.]

Slide 40:

Alterations

- NO MORE “alternate” toilet stalls specified for instances of technical infeasibility; all alterations must comply “to the maximum extent feasible”

[Image: Figure 30(b) shows two designs for toilet stalls that do not fully comply with 1991 Standards for new construction, but include some accessible features. an "X" superimposed on the figure indicates these specifications are no longer included in the 2010 Standards.]

Slide 41:

Swinging Doors

- New exception

  - Doors may swing over fixture clearances in single-user toilet rooms if clear floor space (at least 30” X 48”) is available beyond the arc

[Image: Diagram shows a clear floor space, 30 inches by 48 inches, located outside the arc of the door that swings into a single-user toilet room; the door swings over the separate clear floor space required at the toilet.]

Slide 42:

Toilets: Centerline

- Standard: 16” – 18”

- Ambulatory: 17” - 19”

[Image: Figure shows toilet centerline position in relation to near wall or partition: between 16 inches and 18 inches for wheelchair accessible toilets and between 17 inches and 19 inches for toilets in ambulatory accessible compartments.]

Slide 43:

Toilets: CFS

- Clear floor space in standard wheelchair-accessible compartment or single-user room allows side approach

  - Exception for residential dwelling units

[Image: Figure shows clear floor space at a wheelchair-accessible toilet: 60 inches minimum measured from the side wall and 56 inches minimum measured from the rear wall.]

Slide 44:

Toilets: Rear Grab Bar

- New exception allows 24” rear wall grab bar where wall space is limited by adjacent recessed fixture

[Image: Diagram shows 24 inch long grab bar located on limited wall space behind toilet where recessed bathtub is adjacent.]

Slide 45:

Toilets: Paper Dispensers

- 1991:

  - Requirements not specified in text; shown in figures

    - 36” max. from rear wall to front of dispenser

    - 19” min. above floor to centerline of dispenser

- 2010:

  - 7” – 9” in front of toilet to centerline of dispenser (no relation to rear wall)

  - Height of paper outlet 15” - 48” above floor

Slide 46:

Where’s the Paper?

- CAUTION: Not all area indicated by shading is available for location of toilet paper dispenser outlet if dispenser projects from wall: must maintain clearances required for use of grab bar (12” min. above and 1 ½” min. below bar)

[Figure shows required position of toilet paper dispenser outlet between 7 inches and 9 inches in front of the leading edge of the toilet, and between 15 inches and 48 inches above the floor.]

Slide 47:

Chapter 7: Communication Elements and Features

Highlights

Slide 48:

What’s in Chapter 7?

- 701 General

- 702 Fire Alarm Systems

- 703 Signs

- 704 Telephones

- 705 Detectable Warnings

- 706 Assistive Listening Systems

- 707 Automatic Teller Machines and Fare Machines

- 708 Two-Way Communications Systems

Slide 49:

Fire Alarm Systems [Image indicates scoping provisions]

- Employee work areas with audible alarm coverage: wiring system must be designed to facilitate future integration of visible alarm devices

- Visible alarms not required in existing facilities unless existing alarm system upgraded or replaced, or new system installed

Slide 50:

Fire Alarms

- Standards reference model code (NFPA 1999 or 2002) to a great extent (which allows some visible alarms to be mounted on ceilings), but …

  - Both audible and visible alarms must be permanently installed (yes, in communication-accessible hotel rooms, too!)

  - Sound level of audible alarms not to exceed 110 dB

Slide 51:

Signs

- Location of tactile signs

[Image: Figure shows a space, a minimum of 18 inches by 18 inches square, located outside the arc of a swinging door; the space is centered on the centerline of a tactile sign mounted on the wall next to the latch side of the door.]

[Image: Figure illustrates the mounting height of a tactile sign; 48 inches minimum to the bottom of the lowest tactile characters and 60 inches maximum to the bottom of the highest tactile characters.]

Slide 52:

Detectable Warnings [Image indicates scoping provisions]

- 1991:

  - Curb ramps

  - Hazardous vehicular areas

  - Reflecting pools

  - Transit platforms

- 2010:

  - Rail platforms only

    - … but don’t forget DOT’s rule for transportation facilities!

Slide 53:

Assistive Listening Systems [Image indicates scoping provisions]

- 1991:

- Permanent systems in assembly areas where audible communication is integral and with

  - Occupant load of at least 50 people, OR audio-amplification, AND

  - Fixed seating

- 2010:

- Systems provided in assembly areas where audible communication is integral and with

  - Audio-amplification

  - Courtrooms

Slide 54:

Assistive Listening System Receivers [Image indicates scoping provisions]

- 1991:

- Receivers: 4% of total seating capacity

- 2010:

- Receivers: table (4% in small facilities, fewer in larger facilities)

  - 25% HAC unless entire area looped

  - Can scope combined seating in multiple assembly areas in one building under common management if receivers can be used with all systems

Slide 55:

ATMs and Fare Machines [Image indicates scoping provisions]

- At least one of each type at each location must be accessible

  - If one facility provides both interior and exterior machines, they are considered separate “locations”

[Image: hand inserts card into slot labeled with Braille characters]

Slide 56:

Questions?

Slide 57:

Contact Us

- ADA Questions

  - ADA National Network

    - 1-800-949-4232 V/TTY

    - www.adata.org

- Questions about this presentation

  - Mid-Atlantic ADA Center

    - 1-800-949-4232 V/TTY (DC, DE, MD, PA, VA, WV)

    - 301-217-0124 local

    - www.adainfo.org