Slide 1:

Welcome!

Accessibility and the ADA: Facilities Standards Update will begin at 2:00 p.m. Eastern Time

Slide 2

Listening to the Webinar

- Online:

  - Please make sure your computer speakers are turned on or your headphones are plugged in

  - Control the audio broadcast via the AUDIO & VIDEO panel

  - If you have sound quality problems, please go through the Audio Wizard by selecting the microphone icon

[Image: arrow points to microphone icon on audio and video panel]

Slide 3

Listening to the Webinar (cont.)

To connect by telephone:

1-443-453-0034

Pass Code:

368564

This is not a toll-free number

Slide 4

Captioning

- Real-time captioning is provided; open the window by selecting the “cc” icon in the Audio & Video panel

  - You can re-size the captioning window, change the font size, and save the transcript

[Image: arrow points to the "cc" icon in the audio and video panel]

Slide 5

Submitting Questions

- In the webinar:

  - Double-click on “Mid-Atlantic ADA Center” in the Participant List to open a tab in the Chat panel (keyboard: F-6 and arrow up or down to find Mid-Atlantic ADA Center); type your question in the text box and “enter”

    - Your question will be sent to the presenters; other participants will not be able to see it

- E-mail: ADAtraining@transcen.org

[Image: participant list and chat box]

Slide 6

Technical Assistance

- If you experience technical difficulties

  - Use the Chat panel to send a message to the Mid-Atlantic ADA Center

  - E-mail ADAtraining@transcen.org

  - Call 301-217-0124

Slide 7

Archive

- This webinar is being recorded and can be accessed within a few business days

    - http://adainfo.org/content/AccessibilityandADAWebinars

Slide 8:

Accessibility and ADA: Facility Standards Update

Technical Specifications: Chapters 8 - 10

Slide 9:

Today’s Agenda

- Chapter 8: Special Rooms, Spaces, and Elements

- Chapter 9: Built-In Elements

- Chapter 10: Recreation Facilities

- Questions

Slide 10:

Chapter 8: Special Rooms, Spaces, and Elements

Highlights

Slide 11:

What’s in Chapter 8?

- 801 General

- 802 Wheelchair Spaces, Companion Seats, and Designated Aisle Seats

- 803 Dressing, Fitting, and Locker Rooms

- 804 Kitchens and Kitchenettes

- 805 Medical Care and Long-Term Care Facilities

- 806 Transient Lodging Guest Rooms

- 807 Holding Cells and Housing Cells

- 808 Courtrooms

- 809 Residential Dwelling Units

- 810 Transportation Facilities

- 811 Storage

Slide 12:

Assembly Area Seating [Image indicates scoping provisions]

- Slightly increased scoping for wheelchair seating locations in certain smaller venues

- Significantly decreased scoping in larger venues

- Much more detailed requirements for dispersion, including regulatory requirements added to guidelines by DOJ

  - Stadium-style movie theaters

  - Temporary platforms/temporary seating

Slide 13:

Kitchens and Kitchenettes

- New specifics for appliance controls, storage space, work surfaces, maneuvering clearances, and clearances at appliances and fixtures

  - Requirements and allowances for kitchens in residential dwelling units

  - Added regulatory requirements for kitchens in housing at places of education

Slide 14:

Pass-Through Kitchens

[Figure shows pass-through kitchen with two entry points, one at each end, and minimum clearance of 40 inches between opposing cabinets and appliances on each side.]

Slide 15:

U-Shaped Kitchens

[Figure shows two diagrams of U-shaped kitchens, each with one entry. Clearance of 60 inches minimum is provided between opposing cabinets, appliances, and walls.]

Slide 16:

No-Cook Kitchens

- Exceptions for kitchen without cook top or conventional range

  - Standard clearances (40” min. for pass-through or 60” min for U-shaped) not required

    - Accessible route still required

  - Parallel approach allowed to sink

    - Other accessible features still required (height 34” max., accessible faucet, etc.)

Slide 17:

Medical Care Facilities

- DOJ regulations require medical care facilities that do not specialize in the treatment of conditions that affect mobility to disperse accessible patient bedrooms “in a manner that is proportionate by type of medical specialty”

[Image: prescription pad]

Slide 18:

Transient Lodging [Image indicates scoping provisions]

- Charts detail scoping requirements for mobility-accessible rooms and communication-accessible rooms

  - At least one of the mobility-accessible guest rooms shall also be equipped for communication accessibility, but

  - Not more than 10% of mobility-accessible guest rooms shall be used to satisfy the requirement for communication-accessible rooms

Slide 19:

Transient Lodging: Multiple Buildings on a Site [Image indicates scoping provisions]

- Title III Regulations

  - Separate facilities, built on a common site under one building permit, may combine the number of total rooms to determine scoping IF each facility has fewer than 50 rooms

  - Such facilities are scoped separately if they have more than 50 rooms

[Image: Resort with multiple lodging buildings set in snowy mountain valley]

Slide 20:

Dispersion [Image indicates scoping provisions]

- Dispersion among classes, types, etc.

  - When minimum number does not allow complete dispersion, follow priorities:

    - Type

    - Number of beds

    - Amenities

Slide 21:

Alterations [Image indicates scoping provisions]

- Alterations

  - Scope limited additions/alterations projects separately until new construction scoping levels are achieved

Slide 22:

Alterations: Advisory [Image indicates scoping provisions]

- Alterations ADVISORY

  - In alterations and additions, the minimum required number of accessible guest rooms is based on the total number of guest rooms altered or added instead of the total number of guest rooms provided in a facility. Typically, each alteration of a facility is limited to a particular portion of the facility. When accessible guest rooms are added as a result of subsequent alterations, compliance with 224.5 (Dispersion) is more likely to be achieved if all of the accessible guest rooms are not provided in the same area of the facility.

Slide 23:

Accessible Guest Rooms

- What’s new in the rooms

  - Changes that apply to all types of facilities (toilet centerline position, transfer space at toilets, allowances related to rear wall grab bars, toilet paper dispenser position, features of hand-held shower spray units, permanently installed visible alarm signal devices, etc.), plus …

    - Vanity counter space provided in accessible rooms must be comparable to that provided in non-accessible rooms

Slide 24:

Sample Plans: Accessible Guest Rooms

[Figure shows plan view of mobility-accessible hotel guest room, showing clear floor spaces and maneuvering clearances at bathroom fixtures, doors, bed, and window.]

Slide 25:

Housing: Places of Education [Image indicates scoping provisions]

- DOJ regulations require housing at places of education to follow TRANSIENT LODGING provisions, plus

  - Accessible route throughout multi-bedroom units that include mobility-accessible sleeping room(s)

  - Turning space provided in each room served by accessible route

  - Accessible kitchen, including turning space and an accessible work surface

Slide 26:

Housing at Places of Education: Exception [Image indicates scoping provisions]

- Apartments or townhouses leased year-round exclusively to graduate students or faculty, which do not contain any public or common use areas available for educational programming, are subject to requirements for residential facilities (not transient lodging requirements)

Slide 27:

“Elevator Exemption” [Image indicates scoping provisions]

- Distinction between Title II and Title III

  - Application of transient lodging standards to housing at places of education means entities can not use elevator exemption allowed for residential facilities, however …

  - Traditional elevator exemption available to private entities (fewer than 3 stories OR fewer than 3000 sq. ft. per story) is unchanged

Slide 28:

Detention and Correctional Facilities [Image indicates scoping provisions]

- DOJ: regulatory additions under Title II

  - Increased scoping for mobility-accessible cells: 3%

    - Dispersed among classification levels

  - Requirements for alterations to eventually achieve 3% mobility-accessible cells

    - May use comparable “substitute” cells

[Image: prison cells]

Slide 29:

More on Jails and Prisons [Image indicates scoping provisions]

- Special cells (detoxification, medical isolation, protective custody, etc.)

  - One of each type mobility-accessible

- Communication access

  - 2% of general purpose cells

- Requirements for visiting areas

Slide 30:

Social Service Centers [Image indicates scoping provisions]

- DOJ regulations require social service center establishments (e.g. group homes, halfway houses, shelters) that provide temporary sleeping accommodations or residential dwelling units to comply with standards for residential facilities, plus …

Slide 31:

Social Service Centers: Accessible Features [Image indicates scoping provisions]

  - In sleeping rooms with more than 25 beds, minimum 5% of beds need clear floor space on both sides, or between two beds, for parallel approach

  - Facilities with more than 50 beds that provide common-use bathing facilities need at least one roll-in shower with a seat, or, if gender-separate facilities are provided, at least one for each gender

    - Transfer-type showers are not permitted in lieu of a roll-in shower with a seat

    - Exceptions allowed for typical residential dwelling units are not permitted (i.e. grab bars and shower seats must be installed, not merely reinforcements in walls to support future installation)

Slide 32:

Residential Units for Sale: Title II [Image indicates scoping provisions]

- DOJ regulations

  - Units designed and constructed or altered for sale to individual owners must comply with standards for residential facilities

  - Units designed and constructed for specific buyers must also comply; accessible units go to pre-identified buyers with disabilities who request them

Slide 33:

Residential Dwelling Units: Mobility Features

- Exceptions allowed

  - Adjustable-height sinks

  - “Adaptability” for grab bars, shower seats, and cabinetry under lavatories and sinks

  - Toilet seat height permitted 15” to 19” above the finish floor

  - Lavatory permitted 18” from toilet centerline (to near edge of lavatory) where clearance of at least 66”, measured from the rear wall, is available around the toilet

Slide 34:

Residential Unit Toilet Allowance

Figure 604.3.2 (Exception) Overlap of Water Closet Clearance in Residential Dwelling Units

[Figure 604.3.2 illustrates the exception allowed for a lavatory within 18 inches of the toilet centerline in a residential dwelling unit where the clear floor space is 60 inches (measured from the side wall adjacent the toilet) by 66 inches (measured from the rear wall).]

Slide 35:

Residential Dwelling Units: Communication Features

- Fire alarm/smoke detection: system wiring/visible and audible device in unit, where systems/devices are provided

- Visible signal for doorbell

- Means to visually identify visitor at door (door scope)

- Two-way communication systems, where provided, support voice and TTY

Slide 36:

Chapter 9: Built-In Elements

Highlights

Slide 37:

What’s in Chapter 9?

- 901 General

- 902 Dining Surfaces and Work Surfaces

- 903 Benches

- 904 Check-Out Aisles and Sales and Service Counters

Slide 38:

Accessible Benches

- Size dimensions: 42” long minimum and depth 20” – 24”

- Clarification that clear floor space is parallel to short end of bench

- May be affixed to wall or have specified back support

[Figure shows bench with back support positioned 2 inches maximum to 18 inches minimum above the seat surface and 2 1/2 inches maximum from the rear edge of the seat measured horizontally.]

Slide 39:

Chapter 10: Recreation Facilities

Highlights

Slide 40:

What’s in Chapter 10?

- 1001 General

- 1002 Amusement Rides

- 1003 Recreational Boating Facilities

- 1004 Exercise Machines and Equipment

- 1005 Fishing Piers and Platforms

- 1006 Golf Facilities

- 1007 Miniature Golf Facilities

- 1008 Play Areas

- 1009 Swimming Pools, Wading Pools, and Spas

- 1010 Shooting Facilities with Firing Positions

Slide 41:

Amusement Rides [Image indicates scoping provisions]

- GENERAL EXCEPTION

  - Mobile or portable (traveling carnivals, fairs, etc.)

- EXCEPTIONS from requirement to provide wheelchair seating space, transfer seat, or transfer device

  - Operated by rider (e.g. bumper cars)

  - Primarily for children, adult assistance on and off

  - Rides with no seats (e.g. Roundup)

Slide 42:

Boating Facilities [Image indicates scoping provisions]

- Boat slips: a portion of a fixed or floating pier used for berthing (transient or long term), or for getting on and off boats

- Accessible boat slips provided according to scoping table, dispersed among types

  - Where slips are not marked, 40 feet = 1 slip

- Boarding piers at boat launch ramps: 5%

Slide 43:

Gangways

- Requirements apply to gangways that connect a fixed facility or land with a floating structure, not a vessel

- Exceptions for gangways

  - No “resting platforms” required

  - Slopes should not exceed 1:12, but gangways do not have to be longer than 80 feet, or, in facilities with fewer than 25 boat slips, gangways do not have to be longer than 30 feet

Slide 44:

Exercise Machines [Image indicates scoping provisions]

- At least one of each type must provide clear floor space, positioned for transfer

[Image: individuals in a gym work on various types of exercise machines]

Slide 45:

Fishing Piers and Platforms

- Exceptions for gangway slopes

  - Gangways do not have to be longer than 30 feet

- Where railings are provided, 25% accessible, dispersed

  - Railing no higher than 34”, accompanied by edge protection OR surface extension with toe clearance under railing

[Image: accessible fishing position with lowered railing and deck surface extension, including toe clearance under railing to allow individual using wheelchair to pull up]

Slide 46:

Golf Courses

- Accessibility is based on golf cars, not wheelchairs

  - 48” wide min. passages and accessible routes on course and to related spaces where golf cars may be used (weather shelters, bag drop, etc.)

  - 60” x 96” min. clear space in weather shelters

  - Handrails not required on course; if provided, route or passage must be 60” wide min.

Slide 47:

Miniature Golf [Image indicates scoping provisions]

- 50% of holes must be accessible

- Accessible holes must be consecutive

  - One break allowed if last hole in sequence is last hole in course

- Golfer must be able to exit facility after final hole without traveling back through other holes

Slide 48:

Accessible Mini-Golf

- Accessible routes can be on or adjacent to the playing surface (or combination of both)

  - Some exceptions allowed for slopes, handrails, and landings on ramps; 1” curbs where accessible route intersects playing surface

- “Golf club reach range”

  - Any place ball may come to rest can be no more than 36” from accessible space (running slope up to 1:20 allowed) connected to accessible route

Slide 49:

Miniature Golf Club Reach Range

[Figure shows the accessible area needed to ensure that miniature golfers can reach the ball with their golf clubs.]

Slide 50:

Play Areas

- Understanding definitions is essential!

  - Play component

  - Ground level play component

  - Elevated play component

  - Soft contained play structure

  - Use zone

[Image: A free-standing spiral slide is a ground level play component because the user enters and exits from ground level.]

Slide 51:

Water Play Components

- Remember that requirements for water play components are addressed as “play areas” (not swimming pools)!

[Image: water play area]

Slide 52:

Swimming Pools, Wading Pools, and Spas [Image indicates scoping provisions]

[Table outlines requirements for means of pool access:

Small swimming (under 300 linear feet of pool wall: only 1 means required AS LONG AS one is sloped entry or lift

Large Swimming (300 or more linear feet of pool wall): 2 means required. Primary means must be sloped entry or lift; secondary means can be any permitted type, including sloped entry, lift, transfer wall, transfer system, or accessible pool stairs

Pools where user access limited to one area (wave action, leisure river, etc.): may choose sloped entry, lift, or transfer system

Wading: sloped entry

Spa: may choose either lift, transfer wall, or transfer system]

Slide 53:

Questions?

Slide 54:

Contact Us

- ADA Questions

  - ADA National Network

    - 1-800-949-4232 V/TTY

    - www.adata.org

- Questions about this presentation

  - Mid-Atlantic ADA Center

    - 1-800-949-4232 V/TTY (DC, DE, MD, PA, VA, WV)

    - 301-217-0124 local

    - www.adainfo.org