Slide 1

Good Plans Gone Bad: Top 10 Accessibility Issues and Mistakes will begin at 2 pm ET

Slide 2

About Your Hosts…

TransCen, Inc.

Improving lives of people with disabilities through meaningful work and community inclusion

Mid-Atlantic ADA Center, a project of TransCen, Inc.–Funded by National Institute on

Disability, Independent Living, and Rehabilitation Research (NIDILRR), Administration for Community Living, U.S. Department of Health and Human Services

[Images: Transcen logo, Mid-Atlantic ADA Center logo National institute of Disability, Independent Living and Rehabilitation Research logo]

Slide 3

Listening to the Webinar

Online:

- Please make sure your computer speakers are turned on or your headphones are plugged in

- Control the audio broadcast via the AUDIO & VIDEO panel

- If you have sound quality problems, please go through the Audio Wizard by selecting the microphone icon

[image: arrow points to microphone icon on audio and video panel]

Slide 4

Listening to the Webinar (cont.)

To connect by telephone:

1-857-232-0476

Pass Code:

368564

This is not a toll-free number

Slide 5

Captioning

Real-time captioning is provided; open the window by selecting the “cc” icon in the Audio & Video panel

- You can re-size the captioning window, change the font size, and save the transcript

[image: arrow points to the "cc" icon in the audio and video panel]

Slide 6

Submitting Questions

- In the webinar platform:

  - You may type and submit questions in the Chat Area Text Box or press Control-M and enter text in the Chat Area. You will not be able to see the question after you submit it but it will be viewable by the presenters

  - If you are connected via a mobile device you may submit questions in the chat area within the App

- Questions may also be emailed to: ADAtraining@transcen.org

[image: Participant list]

Slide 7

Customizing Your View

Resize the Whiteboard where the Presentation slides are shown to make it smaller or larger by choosing from the drop down menu located above and to the left of the whiteboard. The default is “fit page”

[image: Resizing dropdown box]

Slide 8

Customize Your View continued

Resize/Reposition the Chat, Participant and Audio & Video panels by “detaching” and using your mouse to reposition or “stretch/shrink”. Each panel may be detached using the page icon in the upper right corner of each panel

Slide 9

Technical Assistance

If you experience technical difficulties

- Use the Chat panel to send a message to the Mid-Atlantic ADA Center

- E-mail ADAtraining@transcen.org

- Call 301-217-0124

Slide 10

Archive

- This webinar is being recorded and can be accessed within a few weeks

- You will receive an email with information on accessing the archive

Slide 11

Certificate of Participation

- Please consult the reminder email you received about this session for instructions on obtaining a certificate of participation for this webinar.

- You will need to listen for the continuing education code which will be announced at the conclusion of this session.

- Requests for continuing education credits must be received by 12:00 PM EDT November 11, 2016

Slide 12

Top 10 errors and omissions for building access

Based on the 2015 International Building Code®and the ICC A117.1 -2009 Accessible and Usable Buildings and Facilities & the 2010 ADA Standards

Presenter: Dom Marinelli, Accessibility Services, United Spinal Association

Slide 13

Approach for this discussion -

- We are going to make basic statements and decide if they are true or false

- We will run through the basic requirements

- Then we will look at real life examples to see good and bad examples

- Sometimes we will also look at items closely related

Slide 14

Top 10 -Example

The code official can require barrier removal on existing building.

True or false

Slide 15

Role of the Code Official

- The code official has the right to enter and inspect when a building is being altered.

- They enforce the adopted code and any state laws.

- Enforcement is during plan review and inspections.

- They cannot require a building owner to update or make improvements unless the building has code violations and is a public safety hazard.

[image: Cartoon of an inspector looking at a house]

Slide 16

Enforcement of Federal Requirements

Complaints

[image: Two people talking about a complaint]

[image: wheelchair on steps - symbolizing no accessibility]

Inspection and Review

[image: Cartoon of an inspection form]

Through the courts

[image: a judge's gavel]

Mediation

[image: a group of people discussing a compromise]

Slide 17

Top 10 Countdown -10

Construction trailers are not required to be accessible.

True or false

Slide 18

Construction Sites

[image: construction trailer]

Slide 19

Good or Bad?

[image: construction trailer as a sales office]

Slide 20

Top 10 Countdown-9

Churches are not required to be accessible.

True or false

[image: church]

Slide 21

Religious facilities

- The ADA exempts properties owned by religious entities.

- The International Codes consider churches as assembly spaces and requires them to be accessible.

Slide 22

Areas in Places of Religious Worship

- Small areas used for religious ceremonies are not required to be on an accessible route.

- < 300 sq.ft. in area and elevated or lowered >=7 inches

- Balconies with less than 25% of the sanctuary seating are not required to be on accessible route.

[images: different parts of a church including baptismal font and altar]

Slide 23

Top 10 Countdown-8

Protruding objects are not allowed along and accessible route.

[image: man with white cane and protruding fire extinguisher and water fountains]

True or false

Slide 24

Protruding objects

- Protruding objects are limited over circulation paths.

- Objects must have a bottom edge 27” or be above 80”.

- If the object has a bottom edge between 27” and 80” it cannot protrude out more than 4”.

- Where the vertical clearance is less than 80” a barrier with the leading edge less than 27” is required.

Slide 25

Overhead protruding object

[images: arrows point to Overhead protruding object: Underneath stairs]

Slide 26

Overhead protruding object

[images: arrows point to Overhead protruding object: Underneath stairs]

Slide 27

Protruding Objects

[image: Example of protruding object: wall beams]

Slide 28

Protruding Objects

[images:parking signage located in planters so they are not protruding objects]

Slide 29

Protruding object

[image: example of protruding object: Water fountains]

[image: example of protruding object: accessible bar in restaurant]

Slide 30

Protruding object

[image: example of protruding object: Handrails]

[image: handrail extensions as protruding objects]

Slide 31

Handrail Extension

- The handrail extension at the bottom is 1 tread depth minimum and sloped.

- The 2010 ADA has removed the requirement for the additional 12” horizontal extension at the bottom.

- The handrail extension at the top is 12” minimum horizontal.

- The extension must be in the direction of the stairway run

[Diagrams showing handrail extension]

Slide 32

Good or Bad?

Handrail extensions?

[image: stair with handrails that bend to the sides]

Slide 33

Top 10 countdown-7

Curb cuts have the same requirements as ramps.

True or false

Slide 34

Curb cuts

- Curb cuts and ramps are the same for slope and cross slope.

- Landings and curb cuts and ramps shall be designed of prevent the accumulation of water

- Curb cuts and ramps do different requirements of edge protection, landings and handrails.

Slide 35

Cut-in Curb Ramps

[diagram: curb cut ramp with flared sides]

[diagram: curb cut ramp with curbs on both sides]

X = 36” minimum in new construction

On existing sites, if landing is <36” then slope of flared sides shall not exceed 1:12.

Slide 36

Built-Up Curb Ramps

[diagram: built up curb ramp]

On existing sites, if landing is <36” then slope of flared sides shall not exceed 1:12.

Slide 37

Detectable Warnings at Curb Ramps

- Detectable warnings are not required on curb ramps by IBC or A117.1

- If a designer chooses to provide detectable warnings, then technical provisions are provided for area covered, location, pattern and contrast.

[image: detectable warning technical criteria]

Slide 38

Painting at Curb Ramps

- Surfaces are required to be slip resistant, so don’t paint the curb ramp or flared sides

- If the curb is painted, then just the curbs on the flared sides are painted

[image: curb cut that is totally painted]

[image: painted curbs at curb ramp]

Slide 39

Curb Ramp Location

- A 36” minimum landing must be available at the top of the curb ramp

- A depressed sidewalk with curb ramps at each end is permitted

- Don’t put a built up curb ramp overlapping the access aisle

- Locate so that they will not be obstructed by parked cars

[image: curb ramp has no top landing]

[image: depressed landing for curb ramps]

[image: curb ramp overlapping access aisle]

Slide 40

Curb Ramp Allowances

- Curb ramps can have a rise of more than 6 inches.

- Curb ramps do not have to have handrails.

- Curb ramps are not required to have flared sides where there is an adequate landing.

[image: curb ramp with handrails]

[image: curb ramp with rolled curb sides]

Slide 41

Good or Bad?

[Image: depressed sidewalk with curb cuts that have detectable warnings in the wrong place]

Slide 42

Good or Bad?

[image: built-up curb ramp on access aisle]

Slide 43

Good or Bad?

[image: accessible parking spaces with sidewalk between the spaces]

Slide 44

Top 10 countdown -6

All ramps have to slope less than 1:12. Edge protection is 2” high curbs spaces a minimum of 36” apart.

True or false

Slide 45

Ramp Technical Criteria

- >1:20 slope.

- 1:12 slope maximum on accessible routes.

- Change in level at start of ramp

- Surfaces –slip resistant

- Cross slope -< 1:48

- Minimum width –36” between handrails

- Maximum rise –30” between landings

- Adequate landings

Slide 46

Edge Protection, Handrails & Guards

[image: ramp with guard]

>30” drop off

[image: ramp with walls on each side]

No drop off

[image: ramp with bottom rail and no guard]

[image: ramp with curb for edge protection and handrail]

Curb or rail edge protection with <= 30” drop off

Slide 47

Ramp Allowances

- Curved ramps are permitted if they meet cross slope.

- Where the ramp slope matches the sloped floor, edge protection may be provided by a wider surface.

- In assembly seating, accessible ramps are only required for entry and exit from accessible wheelchair spaces.

[image: curved ramp]

[image: assembly seating]

Slide 48

Ramp Allowances

- Barriers may serve as a handrail where guards are not required.

- Projections can be at or below the handrail height.

- Handrail grasping surfaces cannot be obstructed.

[image: ramp in airport]

[image: ramp with supporting posts]

[image: wooden ramp with residential style handrail]

Slide 49

Ramp Allowances

- Ramps can have grilled surfaces in cold or wet areas.

- Where the ramp moves up with the grade, edge protection may be provided by a wider surface

[image: curved ramp in winter environment]

[image: ramp with no edge protection by providing a wider ramp surface]

Slide 50

Good or Bad?

Slide 51

[image: ramp with handrail only. needs edge protection and guards]

Slide 52

[image: ramp to beach - very long]

Slide 53

[image: ramp with one handrail and one guard]

Slide 54

[curved ramp with wire guards]

Slide 55

[image: wide ramp in sports stadium]

Slide 56

Top 10 Countdown -5

Toilet paper dispensers have to be 7”-9” in front of the bowl, measured to the center of the dispenser.

True or false

Slide 57

ADA options for dispensers

Measure to center of dispenser

[diagram showing location for ADA toilet paper]

Slide 58

Good or Bad?

[image: toilet with one small toilet roll]

Slide 59

Good or Bad?

[image: toilet with mega roll dispenser under grab bar]

Slide 60

A117.1 options for dispensers

Measure to the outlet of the paper

[diagram showing dispenser location under grab bar]

[diagram showing dispenser location over grab bar]

[diagram showing dispenser location behind grab bar]

Slide 61

Good or Bad?

[image: toilet with mega roll over grab bar]

Slide 62

Good or Bad?

[image: toilet with dispenser behind grab bar]

Slide 63

Top 10 Countdown -4

All lavatories and sinks are required to be accessible for a front approach.

True or false

Slide 64

Lavatories & Sinks

- Height

- Clearance

- Clear floor space

- Pipe protection

- Controls

[diagram: lavatory requirements]

Slide 65

Slide 66

Good or Bad?

[image: commercial lab]

[image: commercial kitchen]

Slide 67

Good or Bad?

[image: dentist office]

[image:exam room]

Slide 68

Good or Bad?

[image: 4 faucet sink with one bowl]

Slide 69

Good or Bad?

[image: sink with drain to one side]

Slide 70

Good or Bad?

[image: counter with above counter bowls]

Slide 71

Good or Bad?

[image: sink in a day care for children]

Slide 72

Good or Bad?

[image: sink and hand dryer combination]

Slide 73

Good or Bad?

[image: hair washing sinks in a beauty parlor]

Slide 74

Good or Bad?

- Lavatories with enhanced reach range includes water and soap controls (A117.1 606.5).

- Room requirements include towel dispensers or hand dryers (A117.1

- 606.7).

- Other elements covered by operable part requirements.

[image: bathroom towel dispenser garbage can combination]

[image: enhanced reach range sink]

[image: dispensers and changing tables]

Slide 75

Good or Bad?

[image: new style hand dryer where you put your hands down into the machine]

Slide 76

Top 10 Countdown -3

Bottled water fillers can replace the standing drinking fountain.

True or false

Slide 77

Good or Bad?

[image: bottled water dispenser and wheelchair drinking fountain]

Slide 78

Good or Bad?

[image: two drinking fountains - bottled water filler on the standing drinking fountain]

[image: two drinking fountains - bottled water filler on the wheelchair drinking fountain]

Slide 79

Drinking Fountains (Scoping)

- 50% of drinking fountains provided on each floor configured for persons using wheelchairs.

- 50% of drinking fountains provided on each floor configured for standing persons.

- Exception for drinking fountains sized for children

[image: drinking fountain with a child]

Slide 80

Good or Bad?

- One water supply, but bowls will serve two persons.

- The dog fountain exceeds code.

[image: drinking fountain high low with a dog bowl]

[image: child in a wheelchair playing with a dog]

Slide 81

Drinking Fountains (Technical)

- Clear floor space/approach

- Protruding objects

- Operable parts

- Spout location

- Water flow

[image: drinking fountain requirements plan]

[image: drinking fountain requirements elevation]

Slide 82

Good or Bad?

[image: two drinking fountains in an alcove]

Slide 83

Good or Bad?

[image: drinking fountain with side barriers]

Slide 84

Good or Bad?

[image: drinking fountain behind a column]

Slide 85

Good or Bad?

[image: standing drinking fountain with low bottom edge, and wheelchair drinking fountain with knee and toe clearance]

Slide 86

Good or Bad?

[image: drinking fountains with loose benches on each side]

Slide 87

Good or Bad?

[image: recessed drinking fountains]

Slide 88

Top 10 Countdown-2

All restaurants have to have the entire dining area accessible. All types of dining surface have to provide knee and toe clearances.

True or false

Slide 89

Dining Areas

- All dining areas accessible throughout.

  - Exceptions:–Mezzanines with <25% of the total seating.

- Count all seating and standing spaces –5% must be accessible.

- Distributed throughout the facility.

[image: Restaurant: Dining Area]

Slide 90

Good or Bad?

[image: restaurant  with raised booths and banquets]

[image: restaurant with high and low tables]

Slide 91

Good or Bad?

[image: cafe with bar seating - half high and half low]

Slide 92

Good or Bad?

[image: bar seating with portion cut down]

[image: bar seating with portion cut down]

Slide 93

Good or Bad?

[image: bar seating with portion cut down]

[image: bar seating with portion cut down]

Slide 94

Good or Bad?

[image: standing counter with portion cut down]

[image: bar seating with portion cut down]

Slide 95

Good or Bad?

[image: drink rail seating]

[image: cafe table seating]

[image: coffee tables and couches in coffee shop]

Slide 96

Good or Bad?

[image: self service counter]

[image: self service counter]

Slide 97

Tiered seating with tables –Good or Bad?

[image: Tiered seating with tables - dinner theater]

[image: Tiered seating with table - college lecture hall]

Slide 98

Top 10 Countdown -1

Every place you put a cash register is a service window. All service windows have to have a 34” high work surface.

True or false

Slide 99

Built-in Counters

- Check out aisles.

  - Table 1109.12.2 based on number provided.

- Sales and service counters.

  - At least on of each type.

Slide 100

Check-out Counters –Good or Bad?

[image: grocery store counters]

[image: grocery store counters]

Slide 101

Check-out Counters –Good or Bad?

[image: self service grocery counter]

Slide 102

Service Window –Good or Bad?

[image: reception counter]

Slide 103

Service Window –Good or Bad?

[image: customer service at airport]

Slide 104

Service Window –Good or Bad?

[image: service counter in building office]

Slide 105

Service Window –Good or Bad?

[image: bank counter with two counters at one window]

Slide 106

Service Window –Good or Bad?

[image: customer service window with security glaring]

Slide 107

Service Window –Good or Bad?

[image: very narrow customer counter at convenience store]

Slide 108

Built-in Counters

- Built-in counters and work surfaces

  - 5% or work surfaces.

  - 5% of dining surfaces.

- Food service lines:

  - All cafeteria style lines accessible

  - 50% of self service areas.

- Queue and waiting lines:

  - All that serve accessible elements.

Slide 109

Built-in Work Surface –Good or Bad?

[image: work counter in courthouse]

Slide 110

Food Service Line or Service Window –Good or Bad?

[image: restaurant Interior - pick up window]

Slide 111

Food Service –Good or Bad?

[image: self service display]

Slide 112

Food Service Lines –Good or Bad?

[image: cafeteria]

Slide 113

Queue & Waiting Line -Options

[image: queue line requirements]

[image: queue line requirements]

Slide 114

Queue lines –Good or Bad?

[image: ticket window]

[image: queue lines with hard barriers]

Slide 115

Thank you for attending.

Questions?

Slide 116

Today's Presenter

Dominic Marinelli

Vice President

Accessibility Services

United Spinal Association

718-803-3782 ext. 7502

716-713-1768 cell

dmarinelli@accessibility-services.com

Accessibility-Services.com

Slide 117

Contact Us

- ADA questions

  - ADA National Network

    - 1-800-949-4232 V/TTY

    - ADAta.org

- Questions about this webinar

  - TransCen, Inc.

    - 301-424-2002

    - TransCen.org

  - Mid-Atlantic ADA Center

    - 1-800-949-4232 V/TTY (DC, DE, MD, PA, VA, WV)

    - 301-217-0124 local

    - ADAinfo.org

Slide 118

Certificates of Participation

- The continuing education code for this session:

[Listen for code at the conclusion of the session.]

- Please consult your webinar reminder e-mail message for further information on receiving a certificate of participation