Slide 1:

Accessibility and ADA: Facility Standards Update

Technical Specifications: Chapters 3 - 7

Slide 2:

Today’s Agenda

Chapter 3: Building Blocks

Chapter 4: Accessible Routes

Chapter 5: General Site and Building Elements

Chapter 6: Plumbing Elements and Facilities

Chapter 7: Communication Elements

Questions

Slide 3:

Chapter 3: Building Blocks

Highlights

Slide 4:

What’s in Chapter 3?

- 301 General

- 302 Floor or Ground Surfaces

- 303 Changes in Level

- 304 Turning Space

- 305 Clear Floor or Ground Space

- 306 Knee and Toe Clearance

- 307 Protruding Objects

- 308 Reach Ranges

- 309 Operable Parts

Slide 5:

Changes in Level

- 1991: [Figure illustrates a 1/4 inch vertical change in level; figure illustrates a change in level between 1/4 inch and 1/2 inch, beveled at a ratio of 1:2]

- 2010: [Figure 303.3 illustrates a vertical change in level of 1/4 inch combined with an additional 1/4 inch change in level, beveled at a ratio of 1:2, for a total change in level of 1/2 inch]

Slide 6:

Knee Clearance

- 1991: Knee/toe clearances specified in various sections

- 2010: All knee/toe clearance requirements refer to “Building Blocks” section 306

[Figure shows knee clearance 11 inches deep minimum at 9 inches above the finish floor, and 8 inches deep minimum at 27 inches above the finish floor; toe clearance is 9 inches above the finish floor.]

Slide 7:

Reach Range

- 1991:

  - Forward approach: high 48” AFF max.; 15” AFF min.

  - Side approach: high 54” AFF max.; low 9” AFF min.

- 2010: Same for forward or side approach

  - High 48” AFF max.; low 15” AFF min.

- Advisory for children’s reach ranges, based on age groups

Slide 8:

Forward Reach [Figure 308.2.1 illustrates an unobstructed forward reach: high of 48 inches maximum and 15 inches minimum above the floor]

Slide 9:

Chapter 4: Accessible Routes

Highlights

Slide 10:

What’s in Chapter 4?

- 401 General

- 402 Accessible Routes

- 403 Walking Surfaces

- 404 Doors, Doorways, and Gates

- 405 Ramps

- 406 Curb Ramps

- 407 Elevators

- 408 Limited Use / Limited Application Elevators (LULAs)

- 409 Private Residence Elevators

- 410 Platform Lifts

Slide 11:

Routes on Sites

- New exceptions for accessible routes from site arrival points and within sites where the only means of access is by vehicle

  - Separate pedestrian routes not required

    - Where parking or passenger loading zones provided, accessibility required, of course

Slide 12:

Routes between Stories

- New exceptions related to certain multi-story buildings

  - Two-story public building, one story with occupant load of 5 or fewer people and no public use space

  - Detention/correctional facilities, residential facilities, and multi-story accessible transient lodging guest rooms: route not required to stories not containing or serving spaces required to be accessible

  - Air traffic control tower cabs and floor below

- Exceptions are for the routes to the stories only, not for the spaces or elements on the stories

Slide 13:

Routes between Spaces and Elements

- New and revised exceptions

  - “Adaptability” allowed for raised courtroom employee stations (judge’s benches, court reporter’s stations, etc.)

    - NOT for raised public areas (jury boxes, witness stands, attorney areas, etc.)

  - Accessible route to press boxes, except …

    - Located in bleachers, points of entry at one level, aggregate area of all press boxes in facility 500 square feet maximum

    - Free-standing, elevated above grade 12 feet minimum, aggregate area of all press boxes in facility 500 square feet maximum

Slide 14:

Routes in Employee Work Areas

- Common use circulation paths in employee work areas must be accessible except …

  - Located within areas that are less than 1000 square feet and defined by permanently installed partitions, counters, casework, or furnishings

  - Located within areas that are an integral component of work area equipment

  - Located within exterior areas that are fully exposed to the weather

Slide 15:

Accessible Entrances

- 1991: 50% of public entrances, and …

  - Relationship to number of exits required by local codes

  - At least one on ground floor

- If direct connection from parking garage, at least one accessible

- 2010: 60% of public entrances

  - No relationship to exits required by local codes

  - No requirement for ground floor entrance

- If direct connection from parking structure, all accessible

Slide 16:

Doors

- Revised specifications for maneuvering clearances

- Clarification of “recessed” doors

[Figure shows where a recess greater than 8 inches is located outside the maneuvering clearances required for forward approach to a door.]

Slide 17:

Elevators

- New provisions for standard elevators, destination-oriented elevators, and existing elevators

- New sections for limited-use/limited application (LULA) elevators, and residential elevators

Slide 18:

LULAs

- Limited Use/Limited Application (LULA) elevators can be used …

  - Wherever full passenger elevators are not required

  - Wherever platform lifts are allowed

  - Within multi-story residential dwelling units

Slide 19:

Chapter 5: General Site and Building Elements

Highlights

Slide 20:

What’s in Chapter 5?

- 501 General

- 502 Parking Spaces

- 503 Passenger Loading Zones

- 504 Stairways

- 505 Handrails

Slide 21:

Accessible Parking

- New Exemption:

  - Spaces used exclusively for buses, trucks, other delivery vehicles, law enforcement vehicles, or vehicular impound are not required to include accessible spaces as long as public-access lots have accessible passenger loading zones

Slide 22:

Valet Parking

- 1991:

  - Exception for valet parking facilities; accessible spaces not required

- 2010:

  - NO exception for valet parking facilities; accessible spaces required

Slide 23:

Van-Accessible Parking

- 1991:

  - Van-accessible: one of every eight accessible spaces

- 2010:

  - Van-accessible: one of every six, or fraction of six, accessible spaces

Slide 24:

Van-Accessible Parking Configuration

- 1991: Van-accessible space has wider aisle

- 2010: Wider space instead of wider aisle for van spaces

Slide 25:

Access Aisles

- Must be marked to discourage parking in them

- Angled van-accessible parking space access aisles must be on passenger side

Slide 26:

Parking: Signs

- New exemptions

  - Signs not required on sites with four or fewer total parking spaces (including accessible spaces)

  - Signs not required for residential facilities where parking spaces are assigned to specific dwelling units

Slide 27:

Passenger Loading Zones

- At least one accessible passenger loading zone still required at medical care facilities, but no longer required to be “protected from the weather by canopy or roof overhang”

- New requirement for accessible passenger loading zone at vehicle drop-off and pick-up areas at mechanical access parking garages

Slide 28:

Chapter 6: Plumbing Elements and Facilities

Highlights

Slide 29:

What’s in Chapter 6?

- 601 General

- 602 Drinking Fountains

- 603 Toilet and Bathing Rooms

- 604 Water Closets and Toilet Compartments

- 605 Urinals

- 606 Lavatories and Sinks

- 607 Shower Compartments

- 608 Grab Bars

- 609 Seats

- 610 Washing Machines and Clothes Dryers

- 611 Saunas and Steam Rooms

Slide 30:

Drinking Fountains

- 1991:

  - Parallel approach allowed for certain wheelchair-accessible units

- 2010:

  - Forward approach, centered on unit, and knee and toe clearances required for all wheelchair-accessible units

    - Exception for children’s units

  - New specification for spout height for “high” fountains (for standing people):

    - 38” – 43” above floor

Slide 31:

Toilets, Toilet Rooms, and Toilet Compartments

- New Exceptions

  - 50% (rather than all) of “clustered” single-user toilet rooms must be accessible

    - Still 5% for clustered portable single-user toilet or bathing units

  - Toilet rooms in critical or intensive care patient sleeping rooms in medical facilities are NOT required to be accessible

Slide 32:

Ambulatory-Accessible Compartments

- Still required where there are six or more toilet compartments provided, or where there are total of six or more toilets and urinals combined

Slide 33:

Alterations

- NO MORE “alternate” toilet stalls specified for instances of technical infeasibility; all alterations must comply “to the maximum extent feasible”

Slide 34:

Swinging Doors

- New exception

  - Doors may swing over fixture clearances in single-user toilet rooms if clear floor space (at least 30” X 48”) is available beyond the arc

Slide 35:

Toilets: Centerline

- Standard: 16” – 18”

- Ambulatory: 17” - 19”

Slide 36:

Toilets: CFS

- Clear floor space in standard wheelchair-accessible compartment or single-user room allows side approach

  - Exception for residential dwelling units

[Figure shows clear floor space at a wheelchair-accessible toilet: 60 inches minimum measured from the side wall and 56 inches minimum measured from the rear wall.]

Slide 37:

Toilets: Rear Grab Bar

- New exception allows 24” rear wall grab bar where wall space is limited by adjacent recessed fixture

Slide 38:

Toilets: Paper Dispensers

- 1991:

  - Requirements not specified in text; shown in figures

    - 36” max. from rear wall to front of dispenser

    - 19” min. above floor to centerline of dispenser

- 2010:

  - 7” – 9” in front of toilet to centerline of dispenser (no relation to rear wall)

  - Height of paper outlet 15” - 48” above floor

Slide 39:

Where’s the Paper?

[Figure shows required position of toilet paper dispenser outlet between 7 inches and 9 inches in front of the leading edge of the toilet, and between 15 inches and 48 inches above the floor.]

- CAUTION: Not all area indicated by shading is available for location of toilet paper dispenser outlet if dispenser projects from wall: must maintain clearances required for use of grab bar (12” min. above and 1 ½” min. below bar)

Slide 40:

Chapter 7: Communication Elements and Features

Highlights

Slide 41:

What’s in Chapter 7?

- 701 General

- 702 Fire Alarm Systems

- 703 Signs

- 704 Telephones

- 705 Detectable Warnings

- 706 Assistive Listening Systems

- 707 Automatic Teller Machines and Fare Machines

- 708 Two-Way Communications Systems

Slide 42:

Fire Alarm Systems

- Employee work areas with audible alarm coverage: wiring system must be designed to facilitate future integration of visible alarm devices

- Visible alarms not required in existing facilities unless existing alarm system upgraded or replaced, or new system installed

Slide 43:

Fire Alarms

- Standards reference model code (NFPA 1999 or 2002) to a great extent (which allows some visible alarms to be mounted on ceilings), but …

  - Both audible and visible alarms must be permanently installed (yes, in communication-accessible hotel rooms, too!)

  - Sound level of audible alarms not to exceed 110 dB

Slide 44:

Signs

- Location of tactile signs

[Figure shows a space, a minimum of 18 inches by 18 inches square, located outside the arc of a swinging door; the space is centered on the centerline of a tactile sign mounted on the wall next to the latch side of the door; figure illustrates the mounting height of a tactile sign; 48 inches minimum to the bottom of the lowest tactile characters and 60 inches maximum to the bottom of the highest tactile characters.]

Slide 45:

Detectable Warnings

- 1991:

  - Curb ramps

  - Hazardous vehicular areas

  - Reflecting pools

  - Transit platforms

- 2010:

  - Rail platforms only

    - … but don’t forget DOT’s rule for transportation facilities!

Slide 46:

Assistive Listening Systems

- 1991:

- Permanent systems in assembly areas where audible communication is integral and with

  - Occupant load of at least 50 people, OR audio-amplification, AND

  - Fixed seating

- 2010:

- Systems provided in assembly areas where audible communication is integral and with

  - Audio-amplification

  - Courtrooms

Slide 47:

Assistive Listening System Receivers

- 1991:

- Receivers: 4% of total seating capacity

- 2010:

- Receivers: table (4% in small facilities, fewer in larger facilities)

  - 25% HAC unless entire area looped

  - Can scope combined seating in multiple assembly areas in one building under common management if receivers can be used with all systems

Slide 48:

ATMs and Fare Machines

- At least one of each type at each location must be accessible

  - If one facility provides both interior and exterior machines, they are considered separate “locations”

Slide 49:

Questions?

Slide 50:

Contact Us

- Mid-Atlantic ADA Center

  - 1-800-949-4232 V/TTY

  - www.adainfo.org